## Slide 1: How the Thomas Lab Uses Mathematical Modeling: Validation vs Value Wendy Thomas Bioengineering, University of Washington Bioen 485 June 1, 2015

## Slide 2: Why Study Bacterial Adhesion?
Learn to Block Adhesion to Prevent Infection
Bio-inspired Reversible Adhesive to Human Tissue
Minimally invasive surgery
Microrobotics and laproscopics must bind reversibly to move or grab.
Bacteria do this.
Can we learn from them?
Buselli et al Meas. Sci. Technol. 21 (2010) 105802
Adhesion is the first stage in Biofilm Formation
By blocking adhesion, can we prevent infections?
More specific than antibiotics
Bacteria can’t as easily develop resistance.
http://www2.binghamton.edu/biology/faculty/davies/research.htm

## Slide 3: Why Study Adhesion in Flow?
Blood Cells
Platelets and thrombosis
Leukocytes (white blood cells) and inflammation (infection, cancer, vascular disease)
Pathogens and Commensals
Bacteria or viruses
Blood (0.01 – 5 Pa)
Intestines (> 1 Pa)
Urinary tract (< 0.5 Pa)
nutrients
Blood cells and Bacteria must resist forces when binding
1 Pa = 10 dynes/cm2

## Slide 4
α
Fluid Flow
x
y
z
:
Why Use Computational Models?
Chart: 
Test mechanism for how bacterial feet grip
Test mechanism for how bacterial legs stretch
Understand how these mechanisms are important to cell adhesion
models can test mechanisms at molecular and cellular scale
Use models for to design adhesive or anti-adhesive technology
Notes: Explain basic set up, 3D sphere resting on surface, end of fimbriae can form bonds with the surface, driven by laminar fluid flow.
Insert hookean spring and torsional symbols
Bell model rates depend exponentially on force
Gillespie to speed up sims

## Slide 5
Study Bacterial Adhesion in Flow
Low Flow (0.01 Pa)
Medium Flow 0.5 Pa
Syringe
Pump
PPFC
Ligand-coated surface
E. coli
mannose-BSA
Cell expressing receptors
High Flow 2 Pa
free
floating
rolling
stationary
Flow (Shear stress, Pa)
0.01 0.1 1
E. Coli Bugs Stick when the Going Gets Tough

## Slide 6: What Structures may Contribute to this Behavior?
90% of E. coli and other enteric bacteria have
type 1 pili
Tip receptor is called FimH and binds mannose
500 nm = ½ mm
50 nm
glycoproteins on cells
Tip structure:
Le Trong, J Struct Bio 2010
Cell wall is rigid relative to long fimbriae that coat the bacteria
FimH adhesin (bacterial receptor) at tip of each fimbria.
Notes: These E. Coli, like most, are decorated with many long fimbriae.
At the tip of each is the adhesive protein, FimH
One domain of FimH integrates it into the fimbria, while the other is a lectin, or carbohydrate binding protein.
It binds specifically to mannose, a sugar that is on the tips of many glycoproteins expressed on many host cells.

## Slide 7: Part I: Mechanistic Model of Bacterial Feet

## Slide 8: How We Measure Bond Mechanics
ligand-coated cantilever tip
(~ 20 nm across)
Separation, mm
Force, pN
50
0
-50
-100
-150
-200
-250
0 0.2
photodiode
detector
laser light
approach
retract
repulsion
(push)
attraction
(pull)
Method of single molecule force spectroscopy
receptor coated surface
rupture force
Constant speed: measure rupture force
Atomic Force Microscope (AFM)

## Slide 9: Mechanical Properties of FimH-mannose bond
force
0 1 2 3 4
time, seconds
100 -
50-
0-
-50-
-100-
-150-
Standard pull
80 pN pre-load
press
Tensile force induces a much stronger state
Yakovenko JCB 2008
Mannose-BSA
FimH
Standard pulls

## Slide 10
Structural Basis of FimH Catch Bonds
Mechanical Force switches state and causes FimH to Catch
-sheet page turning
finger trap

## Slide 11
no force
with force
Quantitative Model for FimH Catch Bonds
Allosteric (2-state) catch bond model

## Slide 12
Model Fits Data for FimH Catch Bonds:
(Increase force until Rupture)
Models (dotted lines) fit data (solid symbols/lines) at 82, 820, & 8200 pN/sec
Conclude: Yakovenko 2008: FimH forms catch bonds that are enhanced by mechanical force due to allosteric regulation
Preliminary Validation: fit Allosteric Catch Bond Model to Wildtype FimH data
Advanced Validation: predict behavior of of Activated FimH
No new fit!

## Slide 13
How Common are Catch Bonds?
Guo (2006) PNAS
Cell adhesive molecules
Intracellular bonds exposed to force
Integrins
Marshall (2003) Nature
Sarangapani (2004) JBC
Snook (2010) CMB
Kong (2009) J Cell Bio
P-, L- and E-selectin
GPIb/VWF
Yago (2008) J Clin Invest
Actin-myosin
Kinetochore-microtubule complex
Akiyoshi (2010) Nature
Cadherins
Rakshit & Sivasankar (PBS)
Bacterial adhesive molecules
E. coli
FimH/mannose
Yakovenko (2008) JBC
shear-enhanced bacterial adhesion:
E. Coli P-fimbria (Nilsson 2006) &
E. coli CFA/I (Tchesnokova 2010)
Pseudomonas aeruginosa (Lecuyer 2011)
Staphylococcus epidermidis (Weaver 2011)
Streptococcus gordonii (Ding 2010)

## Slide 14: Part II: Mechanistic Model for Bacterial Legs

## Slide 15
Why do we care about Tether Mechanics?
Estimate drag force on cell:
Estimate bond force for single bond:
Longer tethers reduce bond forces

## Slide 16
Forero 2006 PLoS Biology;
Whitfield 2014 PLoS Comp Bio
Mechanical Properties of Fimbrial Arms
E. Coli on surface
Mannosylated cantilever tip
Uncoiling
Uncoiled
Coiled
Fimbrial extension
Force
FimA subunit
E.coli
Tip detaches
Stretch Single Fimbriae
Chart: Elongation
| 0 | 3.1622776601683791E-2 | 6.3245553203367347E-2 | 9.4868329805051568E-2 | 0.12649110640673544 | 0.15811388300841894 | 0.18973665961010291 | 0.2213594362117865 | 0.25298221281347144 | 0.28460498941515522 | 0.31622776601683888 | 0.34785054261852161 | 0.37947331922020755 | 0.41109609582188938 | 0.44271887242357294 | 0.47434164902525688 | 0.50596442562693822 | 0.53758720222862433 | 0.56920997883030811 | 0.60083275543199188 | 0.63245553203368032 | 0.66407830863536177 | 0.69570108523704322 | 0.72732386183872699 | 0.75894663844041543 | 0.79056941504209455 | 0.82219219164378066 | 0.8538149682454621 | 0.88543774484714122 | 0.91706052144882966 | 0.94868329805051577 | 0.98030607465219721 | 1.0119288512538798 | 1.043551627855565 | 1.0751744044572489 | 1.1067971810589341 | 1.1384199576606167 | 1.1700427342623076 | 1.2016655108639838 | 1.2332882874656625 | 1.2649110640673522 | 1.2965338406690359 | 1.32815661727072 | 1.3597793938723981 | 1.391402170474088 | 1.4230249470757657 | 1.4546477236774555 | 1.4862705002791394 | 1.5178932768808218 | 1.5495160534825072 | 1.5811388300841898 | 1.612761606685875 | 1.6443843832875589 | 1.6760071598892501 | 1.7076299364909258 | 1.7392527130926099 | 1.7708754896942944 | 1.8024982662959779 | 1.8341210428976618
spring | 0 | 2.5298 | 5.0596 | 7.5895 | 10.1193 | 12.6491 | 15.1789
entropic polymer | 0 | 0.022761 | 0.045884 | 0.069391 | 0.093308 | 0.11766 | 0.14248 | 0.1678 | 0.19364 | 0.22006 | 0.24708 | 0.27476 | 0.30314 | 0.33228 | 0.36223 | 0.39305 | 0.42483 | 0.45763 | 0.49154 | 0.52666 | 0.56308 | 0.60094 | 0.64035 | 0.68146 | 0.72444 | 0.76947 | 0.81674 | 0.86651 | 0.91901 | 0.97456 | 1.0335 | 1.0962 | 1.1631 | 1.2348 | 1.3117 | 1.3947 | 1.4845 | 1.582 | 1.6884 | 1.805 | 1.9333 | 2.0752 | 2.2331 | 2.4096 | 2.6083 | 2.8333 | 3.0899 | 3.3848 | 3.7265 | 4.1261 | 4.5981 | 5.162 | 5.8441 | 6.6809 | 7.7244 | 9.05 | 10.7712 | 13.0649 | 16.2193
helical coil | 0 | 2.2136 | 4.4272 | 4.6485 | 4.8699 | 4.4272 | 4.6485 | 4.8699 | 4.4272 | 4.6485 | 4.8699 | 4.4272 | 4.6485 | 4.8699 | 4.4272 | 4.6485 | 4.8699 | 4.4272 | 4.6485 | 4.8699 | 4.4272 | 4.6485 | 4.8699 | 4.4272 | 4.6485 | 4.8699 | 4.4272 | 4.6485 | 4.8699 | 4.4272 | 4.6485 | 4.8699 | 4.4272 | 4.6485 | 4.8699 | 4.4272 | 4.6485 | 4.8699 | 4.4272 | 4.6485 | 4.8699 | 4.4272 | 4.6485 | 4.8699 | 4.4272 | 4.6485 | 4.8699 | 4.4272 | 4.6485 | 4.8699 | 4.4272 | 4.6485 | 5.162 | 5.8441 | 6.6809 | 7.7244 | 9.05 | 10.7712 | 13.0649
linear elasticity
yielding elasticity
Strain hardening elasticity
Yielding is not as well understood as strain hardening and linear elasticity
This is called Yielding Elasticity

## Slide 17
Whitfield in preparation
Probing Kinetics of Fimbrial Elasticity
Probing kinetics of phase transitions at various forces
time
position
Zig-zag
hysteresis
No hysteresis
Chart: Elongation Velocity
| 0.1 | 0.5 | 1 | 2 | 5 | 10
uncoil | 55.9181 | 69.4079 | 70.9722 | 78.936 | 87.6589 | 93.8935
recoil | 30.4082 | 23.3742 | 20.1927 | 20.5388 | 19.2929 | 16.975
Chart: Scaled Extension












Flat plateau with hysteresis
sloped plateau at equilibrium

## Slide 18: Quantitative Model of Fimbrial Elasticity
Hookean Spring
Stiffer Worm-like-chain
B
A
C
Chart: Pull Velocity
| 0.1 | 0.5 | 1 | 2 | 5 | 10
uncoil | 55.9181 | 69.4079 | 70.9722 | 78.936 | 87.6589 | 93.8935
recoil | 30.4082 | 23.3742 | 20.1927 | 20.5388 | 19.2929 | 16.975
Chart: Scaled Extension












Softer Worm-like-chain
uncoiling
Flat plateau  cooperative behavior
Hysteresis  slow kinetics
Sloped plateau  Independent events
No hysteresis  fast equilibrium
Worm-like chain = entropic spring;
F  as x  L
overstretching

## Slide 19: Quantitative Model of Fimbrial Elasticity
Chart: Scaled Extension
Where FimH bonds are longest lived
Lines: Simulated uncoiling
Symbols: Experimental data
8-parameter Model
Based on Known Biophysics Mechanisms.
Validated by fitting to data.
Weak validation for mechanism, but good fit to complicated data is enough to incorporate into larger model.

## Slide 20: Yielding Tethers are Common
Yielding tethers have evolved in prokaryotes and eukaryotes
Thomas, W. (2008). "Catch bonds in adhesion." Annu Rev Biomed Eng 10: 39-57
Alpha helix proteins in cytoskeletal spectrin, vimentin also uncoil and yield elastically
These anchor cadherins and integrins, which form catch bonds
Polymers of unfolding domains (fibronectin, fibrinogen, VWF) also yield elastically
They are common in extracellular matrix proteins to which cells bind
Membrane tethers
Bacterial fimbriae

## Slide 21: Part III: Mechanistic Model of Bacterial Adhesion

## Slide 22
Whitfield Biophys J, 2010, and Whitfield in preparation
α
Fluid Flow
x
y
z
:
Bond association proportional to probability of surface contact based on elastic properties and thermal energy (to get xrms):
Bond dissociation according to the Allosteric catch bond model
All but 2 parameters are independently determined
formation and breakage from weak state are fit.
Adhesive Dynamics Simulations:
Chart: 
Fimbrial behavior according to the fimbrial uncoiling model
Fimbrial length and number and bacterial size determined from electron micrographs
Notes: Explain basic set up, 3D sphere resting on surface, end of fimbriae can form bonds with the surface, driven by laminar fluid flow.
Insert hookean spring and torsional symbols
Bell model rates depend exponentially on force
Gillespie to speed up sims

## Slide 23: Fit Two Unknown Parameters
kon and koff were too fast to measure in our experiments, so we vary them to match the shear-dependent switch from free floating to rolling
off-rate
on-rate
Free floating at low flow
Rolling at high flow
Many values worked, as long as they are balanced and fast.

## Slide 24: Validate Simulations
free
floating
rolling
stationary
Experimental
Simulation
Quantitatively compare simulations to experiments:
Moderate to Strong Validation:
Complex data matched with only 2 unknowns
new prediction, but data was already known to us

## Slide 25: Behavior of Bacteria at Low Shear (0.01 Pa)
Green spheres = low affinity bond formed
Bacteria float freely at low flow because few fimbriae touch the surface and most bonds are low-affinity
Analyze what you can’t see in experiments:

## Slide 26: Behavior of Bacteria at Medium Shear (0.25 Pa)
Buckled fimbriae = yellow. Bent fimbriae = angled
Bending and buckling causes stable rolling adhesion

## Slide 27: Behavior of Bacteria at High Shear (1 Pa)
Red = high affinity state 2 bond
Bacteria are stationary when catch bonds activate

## Slide 28: Learn Something New: Effect of Catch Bonds
Rolling
Free floating
Shear Rate (1/s)
Simulate slip bonds
Shear Rate (1/s)
fraction time
stationary
Catch Bonds Cause Switch from Rolling to Stationary
Changed conditions we could not change in expts
Analyzed bonds states like we could not in expts.
Simulate catch bonds
No stationary
Free floating
Rolling
Whitfield, et al Biophysical J (2010):
Change what you can’t change in experiments: make weak slip bonds
Analyze what you can’t see in experiments:
Notes: Why do we want rolling without cbs?
Although the transition to the high-affinity state is force-enhanced, we do not believe it is involved in the shear-enhanced rolling. So we asked…

## Slide 29: Learn Something New: Effect of Fimbrial Elasticity
# of bonds
Shear Rate (1/s)
mm from bacteria to surface
What allows rolling adhesion above a threshold?
More bonds form
Requires correct fimbrial elasticity
5x Stiffer: never roll
5x Softer: always roll
Wildtype: roll only above threshold
# of bonds
Shear Rate (1/s)
Analyze what you can’t see in experiments:
Change things you can’t change in experiments:
Notes: Why do we want rolling without cbs?
Although the transition to the high-affinity state is force-enhanced, we do not believe it is involved in the shear-enhanced rolling. So we asked…

## Slide 30: Validate Simulations at very high Shear:
Chart: Time (s)
Experiments
Chart: Time (s)
 | 1 | 1 | 2.5 | 2.5 | 5 | 5 | 10 | 10 | 15 | 15 | 20 | 20 | 25 | 25 | 0.01 | 0.01
Simulations
Validate simulations
Bacteria creep forward but remain bound as flow is increased

## Slide 31: Learn Something New: Fimbriae Stretch
Bacteria creep forward as fimbriae stretch
As shear stress increases, more catch bonds are activated (red).
When flow is turned down, bacteria moves backwards, activating bonds on the other side.
see what you can’t see in experiments:

## Slide 32: Learn Something New:
Chart: Time (s)
As flow increases, more bonds activate but force per bond is the same at 50 pN.
If flow is turned off, more bonds activate and force per bond is still 30 pN.
analyze things you can’t see in experiments:

## Slide 33: Learn Something New: Effect of Yielding
Is Elastic yielding important?
Or is any kind of stretching enough?
Chart: Elongation
| 0 | 3.1622776601683791E-2 | 6.3245553203367347E-2 | 9.4868329805051568E-2 | 0.12649110640673544 | 0.15811388300841894 | 0.18973665961010291 | 0.2213594362117865 | 0.25298221281347189 | 0.28460498941515538 | 0.31622776601683888 | 0.34785054261852161 | 0.37947331922020838 | 0.41109609582188938 | 0.44271887242357294 | 0.47434164902525688 | 0.50596442562693733 | 0.53758720222862433 | 0.56920997883030811 | 0.60083275543199188 | 0.6324555320336821 | 0.66407830863536266 | 0.69570108523704322 | 0.72732386183872699 | 0.75894663844041721 | 0.79056941504209455 | 0.82219219164378154 | 0.8538149682454621 | 0.88543774484713944 | 0.91706052144882966 | 0.94868329805051665 | 0.98030607465219721 | 1.0119288512538798 | 1.043551627855565 | 1.0751744044572489 | 1.1067971810589341 | 1.1384199576606167 | 1.1700427342623103 | 1.2016655108639838 | 1.2332882874656601 | 1.2649110640673522 | 1.2965338406690359 | 1.32815661727072 | 1.3597793938723957 | 1.391402170474088 | 1.4230249470757634 | 1.4546477236774555 | 1.4862705002791394 | 1.5178932768808218 | 1.5495160534825072 | 1.5811388300841898 | 1.612761606685875 | 1.6443843832875589 | 1.6760071598892525 | 1.7076299364909258 | 1.7392527130926099 | 1.7708754896942944 | 1.8024982662959779 | 1.8341210428976618
spring | 0 | 2.5298 | 5.0596 | 7.5895 | 10.1193 | 12.6491 | 15.1789
entropic polymer | 0 | 0.022761 | 0.045884 | 0.069391 | 0.093308 | 0.11766 | 0.14248 | 0.1678 | 0.19364 | 0.22006 | 0.24708 | 0.27476 | 0.30314 | 0.33228 | 0.36223 | 0.39305 | 0.42483 | 0.45763 | 0.49154 | 0.52666 | 0.56308 | 0.60094 | 0.64035 | 0.68146 | 0.72444 | 0.76947 | 0.81674 | 0.86651 | 0.91901 | 0.97456 | 1.0335 | 1.0962 | 1.1631 | 1.2348 | 1.3117 | 1.3947 | 1.4845 | 1.582 | 1.6884 | 1.805 | 1.9333 | 2.0752 | 2.2331 | 2.4096 | 2.6083 | 2.8333 | 3.0899 | 3.3848 | 3.7265 | 4.1261 | 4.5981 | 5.162 | 5.8441 | 6.6809 | 7.7244 | 9.05 | 10.7712 | 13.0649 | 16.2193
helical coil | 0 | 2.2136 | 4.4272 | 4.6485 | 4.8699 | 4.4272 | 4.6485 | 4.8699 | 4.4272 | 4.6485 | 4.8699 | 4.4272 | 4.6485 | 4.8699 | 4.4272 | 4.6485 | 4.8699 | 4.4272 | 4.6485 | 4.8699 | 4.4272 | 4.6485 | 4.8699 | 4.4272 | 4.6485 | 4.8699 | 4.4272 | 4.6485 | 4.8699 | 4.4272 | 4.6485 | 4.8699 | 4.4272 | 4.6485 | 4.8699 | 4.4272 | 4.6485 | 4.8699 | 4.4272 | 4.6485 | 4.8699 | 4.4272 | 4.6485 | 4.8699 | 4.4272 | 4.6485 | 4.8699 | 4.4272 | 4.6485 | 4.8699 | 4.4272 | 4.6485 | 5.162 | 5.8441 | 6.6809 | 7.7244 | 9.05 | 10.7712 | 13.0649
linear elasticity
yielding elasticity
Strain hardening elasticity
Change things you can’t change in experiments:

## Slide 34: Simulations Show Importance of Elastic Yielding
Only yielding elasticity allows bacteria to remain bound

## Slide 35: How Bacteria Resist Very High Shear
Yielding elasticity distributes force equally between multiple bonds, keeping bonds out of the red zone.
Elastic yielding distributes force equally over many fimbriae
Chart: Elongation
| 0 | 3.1622776601683791E-2 | 6.3245553203367347E-2 | 9.4868329805051568E-2 | 0.12649110640673544 | 0.15811388300841894 | 0.18973665961010291 | 0.2213594362117865 | 0.252982212813472 | 0.28460498941515538 | 0.31622776601683888 | 0.34785054261852161 | 0.37947331922020855 | 0.41109609582188938 | 0.44271887242357294 | 0.47434164902525688 | 0.50596442562693711 | 0.53758720222862433 | 0.56920997883030811 | 0.60083275543199188 | 0.63245553203368254 | 0.66407830863536288 | 0.69570108523704322 | 0.72732386183872699 | 0.75894663844041765 | 0.79056941504209455 | 0.82219219164378177 | 0.8538149682454621 | 0.885437744847139 | 0.91706052144882966 | 0.94868329805051665 | 0.98030607465219721 | 1.0119288512538798 | 1.043551627855565 | 1.0751744044572489 | 1.1067971810589341 | 1.1384199576606167 | 1.1700427342623108 | 1.2016655108639838 | 1.2332882874656594 | 1.2649110640673522 | 1.2965338406690359 | 1.32815661727072 | 1.3597793938723952 | 1.391402170474088 | 1.423024947075763 | 1.4546477236774555 | 1.4862705002791394 | 1.5178932768808218 | 1.5495160534825072 | 1.5811388300841898 | 1.612761606685875 | 1.6443843832875589 | 1.6760071598892532 | 1.7076299364909258 | 1.7392527130926099 | 1.7708754896942944 | 1.8024982662959779 | 1.8341210428976618
spring | 0 | 2.5298 | 5.0596 | 7.5895 | 10.1193 | 12.6491 | 15.1789
entropic polymer | 0 | 0.022761 | 0.045884 | 0.069391 | 0.093308 | 0.11766 | 0.14248 | 0.1678 | 0.19364 | 0.22006 | 0.24708 | 0.27476 | 0.30314 | 0.33228 | 0.36223 | 0.39305 | 0.42483 | 0.45763 | 0.49154 | 0.52666 | 0.56308 | 0.60094 | 0.64035 | 0.68146 | 0.72444 | 0.76947 | 0.81674 | 0.86651 | 0.91901 | 0.97456 | 1.0335 | 1.0962 | 1.1631 | 1.2348 | 1.3117 | 1.3947 | 1.4845 | 1.582 | 1.6884 | 1.805 | 1.9333 | 2.0752 | 2.2331 | 2.4096 | 2.6083 | 2.8333 | 3.0899 | 3.3848 | 3.7265 | 4.1261 | 4.5981 | 5.162 | 5.8441 | 6.6809 | 7.7244 | 9.05 | 10.7712 | 13.0649 | 16.2193
helical coil | 0 | 2.2136 | 4.4272 | 4.6485 | 4.8699 | 4.4272 | 4.6485 | 4.8699 | 4.4272 | 4.6485 | 4.8699 | 4.4272 | 4.6485 | 4.8699 | 4.4272 | 4.6485 | 4.8699 | 4.4272 | 4.6485 | 4.8699 | 4.4272 | 4.6485 | 4.8699 | 4.4272 | 4.6485 | 4.8699 | 4.4272 | 4.6485 | 4.8699 | 4.4272 | 4.6485 | 4.8699 | 4.4272 | 4.6485 | 4.8699 | 4.4272 | 4.6485 | 4.8699 | 4.4272 | 4.6485 | 4.8699 | 4.4272 | 4.6485 | 4.8699 | 4.4272 | 4.6485 | 4.8699 | 4.4272 | 4.6485 | 4.8699 | 4.4272 | 4.6485 | 5.162 | 5.8441 | 6.6809 | 7.7244 | 9.05 | 10.7712 | 13.0649
linear elasticity
yielding elasticity
Strain hardening elasticity
The red zone: bonds break fast above 80 pN.
bonds are stretched to different lengths
…and see things you can’t see in experiments:
How much force on each bond?

## Slide 36: Yet More Validation...
Chart: Time (s) after decrease to 0.01 Pa
| 0.65115000000000511 | 1.2896800000000006 | 3.0110399999999977 | 3.3881999999999994 | 4.0138799999999986 | 7.2951000000000015 | 7.38476 | 8.2481399999999994 | 8.2973499999999998 | 11.9253 | 17.121929999999999 | 18.328099999999989 | 20.801250000000035 | 22.090629999999774 | 25.809690000000003 | 26.734760000000001 | 27.388129999999759 | 27.492069999999806 | 27.901339999999788 | 29.51829 | 29.812159999999999 | 38.285160000000012 | 47.907769999999999 | 51.478340000000003 | 52.026970000000013 | 63.661180000000002 | 66.334940000000003 | 70.883960000000002 | 73.084329999999994 | 79.473869999999991 | 96.730199999999996 | 97.936300000000003 | 103.90130000000002 | 129.10959999999992 | 134.74559999999852 | 138.03540000000001 | 138.1071 | 173.38070000000027 | 178.81010000000001 | 293.18529999999993
 | 1 | 0.975 | 0.95 | 0.925 | 0.9 | 0.875 | 0.85 | 0.825 | 0.8 | 0.775 | 0.75 | 0.725 | 0.7 | 0.675 | 0.65 | 0.625 | 0.6 | 0.575 | 0.55 | 0.525 | 0.5 | 0.475 | 0.45 | 0.425 | 0.4 | 0.375 | 0.35 | 0.325 | 0.3 | 0.275 | 0.25 | 0.225 | 0.2 | 0.175 | 0.15 | 0.125 | 0.1 | 0.075 | 0.05 | 0.025
 | 1 | 0.975 | 0.95 | 0.925 | 0.9 | 0.875 | 0.85 | 0.825 | 0.8 | 0.775 | 0.75 | 0.725 | 0.7 | 0.675 | 0.65 | 0.625 | 0.6 | 0.575 | 0.55 | 0.525 | 0.5 | 0.475 | 0.45 | 0.425 | 0.4 | 0.375 | 0.35 | 0.325 | 0.3 | 0.275 | 0.25 | 0.225 | 0.2 | 0.175 | 0.15 | 0.125 | 0.1 | 0.075 | 0.05 | 0.025
 | 1 | 0.97727 | 0.95455 | 0.93182 | 0.90909 | 0.88636 | 0.86364 | 0.84091 | 0.81818 | 0.79545 | 0.77273 | 0.75 | 0.72727 | 0.70455 | 0.68182 | 0.65909 | 0.63636 | 0.61364 | 0.59091 | 0.56818 | 0.54545 | 0.52273 | 0.5 | 0.47727 | 0.45455 | 0.43182 | 0.40909 | 0.38636 | 0.36364 | 0.34091 | 0.31818 | 0.29545 | 0.27273 | 0.25 | 0.22727 | 0.20455 | 0.18182 | 0.15909 | 0.13636 | 0.11364 | 0.090909 | 0.068182 | 0.045455 | 0.022727
 | 1 | 0.9697 | 0.93939 | 0.90909 | 0.87879 | 0.84848 | 0.81818 | 0.78788 | 0.75758 | 0.72727 | 0.69697 | 0.66667 | 0.63636 | 0.60606 | 0.57576 | 0.54545 | 0.51515 | 0.48485 | 0.45455 | 0.42424 | 0.39394 | 0.36364 | 0.33333 | 0.30303 | 0.27273 | 0.24242 | 0.21212 | 0.18182 | 0.15152 | 0.12121 | 0.090909 | 0.060606 | 0.030303
Chart: Time (s) after decrease to 0.01 Pa
| 3 | 4 | 4 | 5 | 5 | 6 | 8 | 8 | 9 | 9 | 9 | 11 | 12 | 13 | 16 | 18 | 19 | 19 | 20 | 21 | 22 | 22 | 23 | 24 | 25 | 28 | 34 | 38 | 42 | 42 | 68 | 70 | 83 | 94 | 100 | 102 | 109 | 130 | 145 | 147 | 167 | 184 | 199 | 218 | 239 | 288 | 300
 | 1 | 0.98649 | 0.97297 | 0.95946 | 0.94595 | 0.93243 | 0.91892 | 0.90541 | 0.89189 | 0.87838 | 0.86486 | 0.85135 | 0.83784 | 0.82432 | 0.81081 | 0.7973 | 0.78378 | 0.77027 | 0.75676 | 0.74324 | 0.72973 | 0.71622 | 0.7027 | 0.68919 | 0.67568 | 0.66216 | 0.64865 | 0.63514 | 0.62162 | 0.60811 | 0.59459 | 0.58108 | 0.56757 | 0.55405 | 0.54054 | 0.52703 | 0.51351 | 0.5 | 0.48649 | 0.47297 | 0.45946 | 0.44595 | 0.43243 | 0.41892 | 0.40541 | 0.39189 | 0.39189
 | 1 | 0.98889 | 0.97778 | 0.96667 | 0.95556 | 0.94444 | 0.93333 | 0.92222 | 0.91111 | 0.9 | 0.88889 | 0.87778 | 0.86667 | 0.85556 | 0.84444 | 0.83333 | 0.82222 | 0.81111 | 0.8 | 0.78889 | 0.77778 | 0.76667 | 0.75556 | 0.74444 | 0.73333 | 0.72222 | 0.71111 | 0.7 | 0.68889 | 0.67778 | 0.66667 | 0.65556 | 0.64444 | 0.63333 | 0.62222 | 0.61111 | 0.6 | 0.58889 | 0.57778 | 0.56667 | 0.55556 | 0.54444 | 0.53333 | 0.52222 | 0.51111 | 0.5 | 0.48889 | 0.47778 | 0.46667 | 0.45556 | 0.44444 | 0.43333 | 0.42222 | 0.42222
 | 1 | 1 | 0.97222 | 0.94444 | 0.91667
 | 1 | 1
E. coli detach at low flow…
unless it is preceded by very high flow
Robust adhesion in variable is critical with peristalsis..
Experiments (previous PNAS paper)
New Simulations
Validation: predict new situation, no new fitting

## Slide 37: CONCLUSIONS: How we used Models:
Value: what we learned: Mostly tested Hypotheses
FimH forms catch bonds that are enhanced by mechanical force due to allosteric regulation
Dynamic properties of fimbriae are consistent with a previously proposed biophysical model for uncoiling.
Catch bonds cause the switch to stationary adhesion in bacteria.
Fimbrial bending causes the switch from free floating to rolling adhesion.
Elastic Yielding helps bacteria stay bound at high flow by distributing force between bonds.
Validation: What made models convincing
Did not fit all parameters to complex behavior; instead, fit many parameters using other data (e.g AFM data of catch bonds, fimbrial stretching and EM images of bacteria). Also makes parameter estimation simpler!
Fit remaining parameters to match limited whole cell data
Used model repeatedly to predict new types of data not used in the fit, or even developed for this validation.
Methods: How did we learn new things? (value)
Analyzed things we couldn’t see in experiments
Changed conditions we couldn’t change in experiments

## Slide 38: In your final projects
Match the level of certainty of the words you use to describe your results to the quality of your validation and verification.
Describe the model results with high certainty if your verification is successful.
Describe what the model tells you about the real system with high certainty only if validation is strong.

## Slide 39: Verification, Validation, Level of Certainty
Is consistent with
May suggest
Suggests
Strongly suggests
Indicates, shows, demonstrates, direct statement w/o qualification
Proves (only use for math proof)
Level of certainty of model results reflects quality of verification
Level of certainty of statement about real system also reflects quality of validation
Good validation adds to verification (less likely to fit data if math is wrong).

## Slide 40
Acknowledgements
Funding
NIH BRP grant
NSF CAREER Award
American Heart Association
University of Washington
Center for Nanotechnology UIF, IGERT
Molecular Biophysics Training Grant
Whitaker Foundation
Colleagues:
Helpful Discussions:
Herbert Hui, Cornell
Nate Sniadecki, UW
Sachin Goyal, Cornell
My Group:
Olga Yakovenko
Matt Whitfield
Tia Ghose
Keith Johnson
Victoria Rodriguez
Kimberly Tran
Jonathon Luo
Suron Woods (REU)
Notes: This work was done in the laboratory of my thesis advisor, Dr Viola Vogel in the department of bioengineering at the univeristy of washington and in collaboration with Dr. Sokurenko in the microbiology department.
I want to acknowledge Elena Trintchina, who did the mutagenesis in the sokurenko lab
Manu Forero who helped with the initial red blood cells assays and did the cell free bead assays in the vogel lab.
Lina Foreor who helped with the bacteria flow chamber assays and did some great inhibitor experiments.
Andre Krammer and David Craig who led the fibronectin SMD research in collaboration with KlausSchulten and UIUC

## Slide 41
Milestone Value Added, due June 1, 2015.
What new knowledge can you learn from analyzing the model, and why might that new knowledge be important?
Consider the following:
What analysis will you do?
How is this knowledge more useful than that you have or can obtain through the experiments needed to validate the model enough to trust the knowledge?
How does this knowledge address different questions from the previous publications that are most related to your project?

## Slide 42: Bond Lifetime at Constant Force
Binding domain No force (SPR)
Whole tip, No force (SPR)
Tip 20 pN
Tip 30-70 pN
Tip 90 pN
Bonds are longer lived at higher force = ‘Catch Bonds’
High-force bond has similar lifetime as isolated binding domain
Low force bond has similar lifetime as full-length FimH
Le Trong Cell 2010

## Slide 43: Computational Issue: How is force transmitted to these force sensors?
Need modeling methods that:
  Span lengths scales – nanoscale to microscale
  Spans time scales: time step fast vs slow relative to relaxation rates
  Address stochastic jump processes (state changes)
  Address stochastic diffusion processes
  Handles objects that can be polymers, particles, surfaces, etc
Need to handle fluids? (CFD?)
Need to handle FEM of some objects?

## Slide 44: When Diffusion dominates
At low Reynold’s numbers, diffusion dominates over inertia
  True for small length scales and longer times
Forces still apply, giving deterministic portion of the equation.
But the velocity and thus momentum of particles does not need to be considered.
Weiner process

## Slide 45: When Inertia Dominates
deterministic equation of motion must take into account both current position (r) and velocity (v). The external forces are taken into account with the acceleration (a).

## Slide 46: Complex Systems:
Even at Low Reynold’s numbers, at small enough times, intertia has an effect
For any given time scale,
  large particles have inertia-dominated behavior
  small particles have diffusion-dominated behavior
So what algorithm can you use?
Need one that is accurate at both extremes, and in between.

## Slide 47: Ermak Monte Carlo Simulations:
These simulations recognize that each particle continues to move deterministically in the same direction for short time periods, but are bombarded with other particles at longer time scales until their motions become uncorrelated.
The relaxation rate, x, at which this occurs is the ratio of the drag coefficient, g, to the mass m:
  x = g / m.
To span these time scales, the position r and velocity v for each degree of freedom is calculated by both deterministic forces (acceleration) and thermal forces (drag and diffusion)

## Slide 48: “Allen and Tildesley*” Ermak Monte Carlo Technique
Add drag and diffusion to 2nd order ODE:
where c0, c1, and c2 are “frictional coeficents” that reflect x, thus drag.
and DrL and DvL are stochastic terms that reflect diffusion
* “computer simulations of liquids” by Allen and Tildesley © 1987

## Slide 49: The Frictional Coefficients:
The frictional coefficients are:
The stochastic terms, (DrL and DvL) are sampled from a bivariate Gaussian distribution with zero mean, and variance:
approaches Weinger process of diffusion dominated situation
approaches Inertia dominated situation

## Slide 50: Significance to Adhesive Technology:
Bioinspired Adhesion: can we learn from bacteria how to make strongly reversible adhesive to human tissue?
Microscale adhesion against applied force:
Just FimH in fimbrial tips
Fimbriae with FimH
Negative control
mannose
As expected, work of adhesion is higher with elastic fimbriae.
Elastic energy contributes to work

## Slide 51: Fimbriae are Needed for Microscale Adhesion
1.5 µm
45 µm
Maximum rupture force
just FimH
fimbriae
neither
Is this due to fimbrial bending or uncoiling? Can’t separate the two experimentally

## Slide 52: FimH Adhesive is Reversible and Self Cleaning
Chart: Pull number
Chart: Fraction
| norm | inhibited | 1 wash | 2 wash | 3 wash
KB91 | 1 | 0.045828 | 0.29692 | 0.72752 | 0.76047
Reversible
Self-cleaning
Do these properties depend on catch bonds or fimbrial bending or uncoiling? Again, easy to test in simulations
Notes: Many promising aspects
Also increased lifetime

## Slide 53: Cause of Rolling to Stationary Switch
“Sticking” of stick & roll adhesion requires catch bonds
Rolling
Stationary
Experimental
Slip bond Simulation
Mostly rolling at medium shear
Mostly stationary at high shear
0.1 1 10
k01 (on) in s-1
k10 (off) in s-1
1 10
Shear Rate (1/s)
catch bonds
Unbound
Bound
k10
k01
slip bonds
fraction time
Shear Rate (1/s)
fraction time
stationary
stationary
Eliminating Catch bonds eliminates stationary adhesion
Time (s)
Distance traveled (mm)
Optimizing slip bond parameters can’t recover the effect
Notes: Add legend

## Slide 54: Do Simulations Match Experiments?
Balanced on- and off-rates from weak state required to reproduce switch from free-floating to rolling adhesion
Simulations Reproduce Stick & Roll Adhesion
Identifying the two unknown parameters
off-rate
on-rate
Free floating
Rolling
free
floating
rolling
stationary
Experimental
Simulation

## Slide 55: Shear Enhanced Adhesion is Common and has Many Potential Advantages
Leukocytes (L-selectin/PSGL-1)
  binding to endothelial cells, patrol blood vessel walls, maintaining a fairly uniform velocity
Platelets (GPIb/VWF):
  Shear enhanced adhesion allows specificity for arterial, not veinous thrombosis.
  Mutations that lose this behavior cause disease
E. coli (FimH/Mannose)
  Stick in high shear regions, where nutrients are rich
  Can move when safe, but stick securely when not.
  Mutations cause commensal bacterial to be pathogenic.
E. coli (P-pili, CFA/ligands).
S. Gordonii (GspB/sTa)
Staph. aureus (Collagen)
Loss of Shear Enhanced Adhesion Causes Disease

## Slide 56
E. coli
E. coli
E. coli
  increase rate of first bond formation once bacteria are near the surface?
  Does shear stress increase rate that additional bonds form?
  Does tension
  increase bond lifetime?
  increase transport of bacteria to surface?
Mechanisms of Shear Enhanced Adhesion
E. coli
E. coli

## Slide 57
What is Reversible Adhesion?
Reversibility
Damages surfaces if detached
Safely removable
Unbinds & rebinds >10X
Strongly reversible
Smart Adhesive;
Self-cleaning
irreversible
reversible
highly reversible
Notes: Our objective is to understand mechanism of shear enhanced adhesion

## Slide 58
BioCatch Adhesive: Strong and Reversible
catch-bond adhesion:
reversible without damage.
nonfouling:
releases ligand when force is removed
Strong receptor-ligand bonds:
tear or damage tissue when detaching
easily fouled by soluble inhibitors or by torn-off surface receptors
FimH: binds to all human tissues
“BioCatch” adhesive